## Slide 2: Fundamentals of Data Communications Network Analysis: Packet and Protocol Analyzers (Wireshark)
Levi Perigo, Ph.D.
University of Colorado Boulder
Department of Computer Science
Network Engineering

## Slide 3: Review

## Slide 4
Notes: Explain why a PC (IP Address 10.1.1.10) plugged into a switchport assigned in VLAN 10, is unable to trace route to any PCs.

## Slide 5: Packet Analysis
  A packet analyzer or packet sniffer is a computer program (or hardware) that can intercept and log traffic that passes over a computer network or part of a network.
    Packet capture is the process of intercepting and logging traffic
  One of the most important tools for a network engineer!

## Slide 6: Network Analysis
The process of listening to and analyzing network traffic
Passive and non-intrusive
Requires strong knowledge of network data flows
  Switch, Router, Firewall
Requires strong knowledge of TCP/IP and protocol communications (IPv6, UDP, ICMP, DHCP, etc.)
  Know the technology, figure out what’s wrong

## Slide 7: Purpose of Network Analysis
Troubleshooting
Security
Network Optimization
Application Analysis

## Slide 8: Troubleshooting Tasks
Locate faulty network devices
Identify device or software misconfigurations
  DNS, DHCP, Rogue Access Point, IPSec
Measure high delays along a path
  Latency via “time” field
  Server TCP SYN/ACK/RST and Slowstart

## Slide 9: Troubleshooting Tasks Cont.
Locate the point of packet loss
  Almost always hardware device
Identify network errors and service refusals
Graph queuing delays

## Slide 10: Security Tasks
Perform intrusion detection (IDS)
  Packets match filter
  Can we perform IPS? What’s the difference?
Identify and define malicious traffic signatures
Passively discover hosts, OS, and services
  Where would we place analyzer?

## Slide 11: Security Tasks Cont.
Log traffic for forensics examination
  Hash files (capinfos)
Capture traffic as evidence
Test firewall blocking
  Outside and inside (make it through?)
Validate secure login and data traversal
  Is traffic encrypted as it should?

## Slide 12: Legal Issues of Listening to Network Traffic (Telecom Policy)
ECPA (Electronic Communications and Privacy Act) “Wiretap Act”
  Prohibits the intentional, actual, or attempted interception, use…electronic communication
Security Issues to Consider
  Define policies regarding use of a traffic capture tool
  Secure files containing network traffic
    PII (Personally Identifiable Information)
    HIPPA & CMI
  Protect against unwanted sniffers
    Block ports
    Wireless passwords
    Top 5 recommendations

## Slide 13: Network Optimization Tasks
Analyze current bandwidth usage
Evaluate efficient use of packet sizes in data transfer applications
Evaluate response times across a network
  Troubleshooting the time between TCP SYN/SYNACK
Validate proper system configurations
  How? Why?

## Slide 14: Application Analysis
Why are applications important to the network?
Analyze application bandwidth requirements
  Get a general summary of bandwidth usage and requirements
  Ports? Time of day?
Identify application protocols and ports in use
Validate secure application data traversal

## Slide 15: Analysis Review - Checklist
Find the top talkers
  Allocate bandwidth appropriately
Identify the protocols and applications used on the network
  Security – IDS
  Baseline
Determine the throughput of applications or network traffic on a link
  Web server, FTP, Mail, etc.
List all hosts communicating on link
  Hosts you don’t recognize or abnormal?
Learn the most common connection problems
Latency and delays

## Slide 16: Analysis Review - Checklist Cont.
Identify and locate misconfigured hosts - How?
  DHCP
  DNS
  Gateway
Recognize segment/network or host that is slowing down traffic
  Top Talkers
    What do you do?
Locate asymmetric traffic prioritization
Graph HTTP flows
  Examine website rates
Identify errors for specific protocol (HTTP, SIP, FTP, etc.)
Build graphs to compare traffic: good, normal, poor

## Slide 17: Analysis Review - Checklist Cont.
Identify applications that do not encrypt traffic
Detect and analyze OS use on network
Replay VoIP conversations to listen to quality
  VoIP Lab
  What else could you do with this information?

## Slide 18: Understand Network Traffic Flows
Switch
  Layer 2 device
  MAC addresses
  Collision domain
  Can’t tell if it has gone through switch (transparent)
Router
  Layer 3 device
  IP addresses
  Broadcast domain
  MAC
  TTL
Firewall, Proxy, NAT/PAT
  Proxy = Layer 4
  PAT = Layer 3 and ”4”
  IP address modifications

## Slide 19: OSI Model Review
Physical
Data Link
Network
Transport
Session
Presentation
Application

## Slide 20: What is Wireshark?
Packet and Protocol Analyzer
  Analyzing Traffic
  Troubleshooting Tasks
  Security Analysis
  Application Analysis
Rated the #1 Open-Source App of all time
  #1 Network Protocol Analyzer
  #1 Network Security Tool

## Slide 21: Wireshark
Typical Uses
  First responder tool!
  Determine Bugs – How?
  Top Talkers
  Slow Response Times and Delayed Traffic
  Network Traffic
  **What is on the wire!
Name changed from Ethereal to Wireshark in 2006 for copyright reasons.
Certification – Wireshark Certified Network Analyst (WCNA) (not recommended)

## Slide 22: How to get it?
You can download for computer FREE at www.wireshark.org.
All Wireshark files are .pcap or .pcapng
  TShark = .pcapng
What version to get?
  Upgrade occasionally
  Stick with what works
Help
  ask.wireshark.org

## Slide 23: Why Wireshark?
Persistent
  Remote/Left on Site
Standardization
  Anyone can read Wireshark
    Vendor specific logs/debugs
Logs/Debugs vs. .pcap
  Logs can be misleading, or they do not capture the whole story
  Debugs can be wrong
    Why?
  .pcap = packets do not lie!

## Slide 24: Wireshark Elements
Capturing Traffic
  Drivers
    NIC – Wireless – Open File
  Capture Filters
    Use Sparingly
      Example: Only capture DNS traffic
    Can’t get that traffic back!
    Use Display Filters instead of Capture Filters
  Wiretap library
    Can open almost any file (not only .pcap)
Network
WinPcap – AirPcap libcap
Capture Filters
Capture Engine

## Slide 25: Processing Packets
Capture Engine
Wiretap Library
Core Engine
(Dissectors/Plugins – Display Filters)
Graphical Toolkit (GTK)

## Slide 26: Place the Analyzer Appropriately
Placement is Key!
  General Rule / Best Practice
    Place Analyzer as close to the complaining user/suspecting unit as possible – Why?
  See from the client’s perspective
    If errors coming from server; then move or add another analyzer to the sever location
  Multiple Locations
    (Problems with this?)

## Slide 27: Where to implement it?
  Depends on the problem and the network configuration
  If you suspect or know that between the client and the server there are some devices that can ‘’mangle’’ the network communications (NAT/Websense appliances, IPSec, firewalls, etc.)
    Capture in multiple places

## Slide 28: Capture Appropriate Traffic
Where do we place it?
  Connecting Analyzer to Switches
    Forward based on target MAC address; doesn’t reach analyzer
    Analyzer Receives Four Types of Traffic
      Broadcast
      Multicast (if configured to pass MCAST)
      Unknown MAC
      Analyzer MAC
Notes: Where to we place it? First, have the class draw/explain where to place the analyzer and then have them explain the packet flow until they realize the traffic doesn’t reach the analyzer.

## Slide 29: Capture Appropriate Traffic - Options
Install on host machine
  Security Issues
    Individual
  Unavailable
  May be unreliable
    CPU Usage
Tap Device
Port Span/Port Mirror
  Switch Capable
  Administrator Capable
Install Hub
  Half-duplex
  Move Device to Hub too!

## Slide 30: Capture Appropriate Traffic
What about a wireless network?
  Promiscuous and/or Monitor Mode
    All traffic
  Need to see Control and Management Frames
  Physically stand by the person/device
    Stand by AP (if all users)
  WISpy adapter and/or AirPCAP adapters

## Slide 31: Wireshark - Tips and Tricks
Display Filters
Statistics
Coloring Rules
Filter, Graph, Analyze

## Slide 32: Display Filters
Error Detection = Green vs. Red
  Keep Typing example:
  ip.addr==255.255.2 (not green) ip.addr==255.255.255.255 (green)
  Just because it is a valid filter doesn’t mean it is appropriate
    Example: HTTP vs. HTTPS

## Slide 33: Display Filters Cont.
Right Click is Easy Method
  Note: Not Selected is Good Option
Apply vs. Prepare
  Apply - takes affect immediately
  Prepare - enters syntax to be changed/modified if needed
    HTTP Errors are 399 and above
    http.response.code == 404 change to http.response.code > 399

## Slide 34: Stats
Statistics
  Top Talker
    Statistics > Conversations > Bytes > Apply as Filter
    Statistics > Endpoints > IPv4 TX bytes > Apply as Filter

## Slide 35: Coloring Rules
  Great to add to different Profiles
  Note: Work in “Top Down” fashion, similar to ACLs

## Slide 36: Filter, Graph, and Analyze Traffic
Expert Info Window
  Button in Bottom Left = Gray vs. Yellow
  Click on Yellow Button; then focus on errors
    Details and Charts are rarely used
Charts and Graphs
  Security
    What protocols clients are using?
    Statistics > Protocol Hierarchy
    Statistics > Conversations
      Check box for Limit to Display Filter
  Graphs
    Statistics > IO Graphs
      Maps throughput download in graph format
      Can alter multiple graphs overlapping to see when/why throughput drops
    Statistics > TCP Steam Graph > Throughput Graph
      Must contain data in packet
    Statistics > TCP Steam Graph > Round Trip Time Graph
    Statistics > HTTP > Requests

## Slide 37: CLI Access
Terminal-based Wireshark
  TShark
TCPDump
Notes: What are the benefits: pro/con?
No remote access, but CLI access
Faster
Advanced filters
Automation and logging and self-healing

## Slide 38: The “Needle in the Haystack” Issue
The #1 reason network engineers shy away from analysis tools
Capture close to client first
Rarely use capture filters
  Okay if you are in the middle of the enterprise – Why?
Use display filters to exclude “good” traffic or focus on “bad” traffic
Colorize “bad” or “questionable” traffic
Add filter expression buttons or specific profiles to quickly find network problems
  Lab
Reassemble for clarity/easy understanding
  “Follow the stream”
Graph for visibility

## Slide 39: Troubleshooting
Notes: Can’t access facebook.com
Incorrect DNS
DNS is down
Wrong default-gateway
Cable unplugged
Gateway router doesn’t have a DR
Sending traffic to Internet, but not getting anything back
  Firewall is blocking that URL

## Slide 40: Questions?

## Slide 41: References
Chappell University
Chapell, L. (2013) Wireshark 101

## Slide 42: Appendix

## Slide 43: The Interface

## Slide 44: How to start a capture
Starting a capture can be done in multiple ways. The most common are:
Select an interface from the interface list: the capture begins immediately with the default option
Click on the Interface List
Click on the one of the two first icons of the ribbon

## Slide 45: How to start a capture
Press Ctrl+E
Use the Capture menu
When you start a capture you can generally choose some options (except when you press CTRL+E or click directly on the interface: In these cases the capture starts immediately).
The most important options you need to know in the option pane are: promiscuous mode, capture filter & enable network name resolution.
CAVEAT: use the enable network name resolution option sparingly! This option will generate a lot of DNS requests and so DNS replies as well. You may not want to generate this kind of traffic.

## Slide 46: Promiscuous mode or not?
In Promiscuous Mode your network interface is going to receive all the traffic even if it is not directed specifically to it. Example: a device (IP 10.14.8.1) is trying to talk with another device (IP 10.14.8.2) on the same network segment. If you are in Promiscuous Mode you should be able to see the conversation even if it is not for you.
There are many factors that may limit your visibility while you are in Promiscuous Mode such as network switches! If your switch is a ‘’proper one’’ should direct the traffic from device A to device B to the switch ports where A and B are physically plugged in.
There are some solutions to this problem: configure the switch to repeat all the traffic to a SPAN port, use an HUB to connect the devices (if you are still able to find one) or ask budget to buy an Aggregating Network TAP)
If you are not in Promiscuous Mode you will be able to see all the traffic direct to you, broadcast and multicast traffic.

## Slide 47: Capture Filters
Some Common and Capture Filters:
ip | Only IP traffic
tcp | Only TCP traffic
udp | Only UDP traffic
host 192.168.0.1 | All the traffic to/for 192.168.0.1
not broadcast and not multicast | Self explanatory
ether src 10:10:EA:11:33:22 | All the Ethernet traffic from that MAC address
ether dst 10:10:EA:11:33:22 | All the Ethernet traffic to that MAC address
ether host 10:10:EA:11:33:22 | All the Ethernet traffic to/for that MAC address
port 80 | Udp or Tcp traffic where the source or destination port is the 80
tcp and udp | Only TCP and UDP traffic

## Slide 48: Display Filters
Display filters: their knowledge is essential to analyze the traffic. They help us to display only the interesting traffic and solve the famous ‘’needle in the haystack” problem
They can be applied while you are capturing or after the capture is finished.
Their syntax is used for Columns definition and coloring rules as well.
Wireshark comes already with a predefined list of filters that can be used as example (starting point)
Display Filters as the Capture Filters are case sensitive ! HTTP is not the same of http
Fortunately when you type filters in the filter field you can use Intellisense.

## Slide 49: Display Filters
To create a filter you can simply type it in the filter field and get the advantage of Intellisense.
Another way to create a filter is to explode a packet in the details section, click on a particular section of it, then right click and choose Prepare Filter or Apply filter.
The difference between apply and prepare is that Apply will immediately apply the filter instead prepare will only prepare the filter in the filter field and then you will need to press the Apply button. The advantage is that you can have a look to the syntax generated and eventually amend it before to apply it.
Another way is to press the Expression button that’s near the Filter field: a GUI to help you to formulate the expression will appear.

## Slide 50: Display Filters
But what about if I want to filter a certain field but I do not know its name?
  The simplest way is to explode the packet and select the field in the Packet Display section and have a look to the Status Bar.
In this case we selected the Do not fragment field and its syntax is ip.flags.df == 1 (1 is set , 0 is not)

## Slide 51
The general structure of a display filter is a sequence of expressions eventually concatenated by logic operators. An expression is a field + comparison operator + value. Example: tcp.dstport == 80
The most common comparison operators are: ==, ||, &&, >=, !=, <=, >, <, matches, contain. For the nostalgic geek it is possible to use the literals eq, or, and, ge, ne,le,gt,lt
&& and || are logic operators
An example: tcp.port == 80 || tcp.port == 443
As with the display filter we need to be careful of the meaning of them
For example tcp && arp is a syntactically valid filter but, won’t match any traffic
Some popular protocols define some basic filters that help us to speed up the writing of filters.
For example instead of writing: tcp.port == 53 || udp.port == 53 we can simply write: dns
Instead of tcp.port==80 ||tcp.port == 443 we can write: http
Other popular protocols are: arp, bootp, smtp, pop3, smb, ftp, ftp-data, ldap, icmp, imap

## Slide 52: Advanced Filters
In some special circumstances we need to match one or more bytes of a packet in specific positions. This type of filter is called offset filter and it is in this form: field (or protocol layer)[offset 0 based:length] comparison value
Example: eth.src[4:2]==22:1f
Example: ip[14:2] == 90:20
To formulate this kind of filter you need to know the protocol well and know what you are looking for.

## Slide 53: Coloring Rules
Coloring Rules and Columns: they are defined with the same syntax used for Display Filters.
  Have you noticed in captures that some packets have a different color from the others?
The Coloring Rules are a very import tool that will help you to better understand the trace file: you will be able to display different kind of packets in a different color and this will help you a lot to find the “needle in the haystack.”
You can manage them via the View -> Coloring Rules menu

## Slide 54: Coloring Rules
Coloring rules color a packet if the rule, expressed with Display Filter syntax, is matched.
Coloring rules can be created, deleted, moved up and down, disabled, imported, exported or reset to default (Cleared).
Coloring rules are saved in the colorfilters file.
Rule precedence: the rules are evaluated from the top to the bottom of the list. When a rule is matched the evaluation finishes for that packet.
How to disable one: Checksum errors*(Most of the time this a false positive error caused by TCP/UDP offloading settings of your network adapter)
To disable it simply select it and then press the disable button. A line will appear on it marking that the rule is disabled. (It is better to disable rules than delete them)

## Slide 55: Columns
Columns are fundamental to view the traffic you captured.
The default column set is not always appropriate for the analysis of all the problems you want to analyse.
So it is possible to define custom columns, resize them and re-arrange them as you like.
Clicking on a column you can sort the data in ascending and descending order: this feature is particularly useful when you order the capture for “Seconds since previous captured/displayed packet”
Custom Column definition needs the field name you want to display: the same field name you use in the Display Filter syntax.

## Slide 56: Creating a New Column
There are many ways to create a custom column: -Edit -> Preferences -> Column section. -Right click on a column and select Column Preferences. -Right click on a field and choose the option Apply as a column: in this case the column definition is applied immediately. If the column definition created is not what you want you will need to edit or remove it using the Column Preferences menu
Column definition is saved in your current profile directory in the preferences file(the active profile is displayed in the right down corner of Wireshark Window)

## Slide 57: Define a Custom Column
Example create a new custom column:
Click on Edit -> Preferences -> Column section.
Click the button.
Select Custom from the Field Type drop down
Enter the field that you want to display in the column in the “Field name” field
Click on the title of the column and name it, then press and then

## Slide 58: Useful Columns to Add
The columns you add depend on the traffic you are going to analyse. You may want to create different configuration profiles for different situations and define a different column set in every profile.
You can reposition the columns, delete them or simply hide them.